## Slide 1: HRI interface comparisons (VR, AR, bio-signal-based) Sebastian Hirt

## Slide 2: Agenda
Specific examples for VR
02
Specific example for AR
03
Specific example for bio-signal-based
04
Why compare?
01
Comparison
05
What is the best path forward?
06

## Slide 3: Why compare?
Best option for current use in industry
Dictate direction of future research
(Tesla, 2022)
(Boston Dynamics, 2022)
Notes: Future robots need interfaces, if not fully autonomous (on the way there anyway)
Swarm control for spot
Spot, robot dog: carrying, surveying, traversing terrain

## Slide 4: Agenda
Specific examples for VR
02
Specific example for AR
03
Specific example for bio-signal-based
04
Why compare?
01
Comparison
05
What is the best path forward?
06

## Slide 5: Specific Example for VR
Control over swarm of robots like a swarm of ants
Oculus Rift headset with Leap Motion
Placing virtual objects in path of robot via environmental manipulation
Zoom in and out of the virtual environment
Teleoperation possible
Intuitive and feasible but might need training
Omnipotent Virtual Giant for Remote Human–Swarm Interaction
(Jang et al., 2021)
Notes: Pick up and placing of robot also possible
N=10 age 20-35 engineering background:
  Test missions are accelerated
  Some actions need training (even with perfect subject!)

## Slide 6: Specific Example for VR
Control robot arms with VR controllers
Oculus Rift headset with default controllers
Teleoperation for work in unsafe environments
Collocation in robot head
Pick up and place blocks
Baxter’s Homunculus: Virtual Reality Spaces for Teleoperation in Manufacturing
(Lipton et al., 2017)
Notes: Consumer grade hardware
Use from save environment
Human can use side cameras in robot arms to align boxes

## Slide 7: Agenda
Specific examples for VR
02
Comparison
05
Specific example for AR
03
Specific example for bio-signal-based
04
What is the best path forward?
06
Why compare?
01

## Slide 8: Specific Example for AR
Visualization of information about robot in shared space
Mobile tablet as camera and controller
Environmental markers on table
Showing range of motion of robot
Pre render potential future moves of the robot
Mobile Mixed-Reality Interfaces That Enhance Human–Robot Interaction in Shared Spaces
(Frank et al., 2017)
Notes: Control via accelerometer
Other methods with cameras:
  Exocentric: on ceiling
  Egocentric: on head (tiltable)
Pretrial better for users with AR plots enabled
No teleoperation (need to be in same environment)

## Slide 9: Agenda
Specific examples for VR
02
Comparison
05
Specific example for AR
03
Specific example for bio-signal-based
04
What is the best path forward?
06
Why compare?
01

## Slide 10: Specific Example for bio-signal-based
Classification of left- and right-hand gestures via muscle signals (EMG)
Error recognition through brain function (EEG)
Combination in hybrid system
Tested on 7 subjects (plug and play) to reduce barrier of entry for new users
Shows potential, but more training data needed for higher reliability
Plug-and-play supervisory control using muscle and brain signals for real-time gesture and error detection
(DelPreto et al., 2020)
Notes: Hit three holes in wall with electric screwdriver
Mistakes can get recognized unconsciously, really fast
N=7, Accuracy: Random choice 70% (15%,15% for wrong targets, 70% for correct one), with human intervention 97%
Neural net classification (error-noerror) only 54% accuracy

## Slide 11: Agenda
Specific examples for VR
02
Comparison
05
Specific example for AR
03
Specific example for bio-signal-based
04
What is the best path forward?
06
Why compare?
01

## Slide 12: General comparison
  VR
    Teleoperation
    Swarm control
  AR
    Display important robot information (range of motion/wear and tear)
  Bio-signal-based
    Control robot with mind (EEG) or muscles (EMG)
Use Cases
(Frank et al., 2017)
(Lipton et al., 2017)
Notes: -VR: different environment, birds eye view
-AR: VR could do the same with front camera, but more expensive
-Bio-signal-based: faster reactions than VR/AR as direct link, but not reliable yet

## Slide 13: General comparison
  VR
    Meta Quest 2/Pro
    Valve Index
  AR
    Tablet/Smartphone
    Google Glasses
  Bio-signal-based
    Wrist band
    Electrode hat
Devices
(Lipton et al., 2017)
(Frank et al., 2017)
(DelPreto et al., 2020)
Notes: -VR: consumer grade devices, default controllers or razer hydra hand trackers; also, smartphone possible, but low res, not as powerful
-AR: consumer grade devices
-Bio-signal-based: maybe Implants at some point, often custom made (expensive)

## Slide 14: General comparison
  VR
    Expensive Headsets
    Cheaper through consumer products
  AR
    Low end cheapest solution
    High end more expensive than low end VR
  Bio-signal-based
    Difficult to evaluate, mostly custom devices
Cost
Technology | Device | Cost ($)
VR | Meta Quest 2 | 450
VR | Valve Index | 1079
AR | I-Pad | 449
AR | Galaxy Tab S8 | 200
AR | Google Glasses | 999
Bio-signal-based | EEG electrode hat | 1500
Notes: -VR: mass market products; high end PC required
-AR: no PC required, controller and screen in one
-Bio-signal-based: maybe Implants at some point, often custom made (expensive)

## Slide 15: General comparison
  VR
    Taking over control of “almost fully” autonomous systems remotely
  AR
    Integration into traditional glasses or even contact lenses
    Increase trust in everyday robots
  Bio-signal-based
    Implants/EEG: huge potential to merge with robots and full control of a robot with a human's thoughts
Future potential
Notes: VR: help in dangerous environments remotely
AR: show future actions of robots to increase trust
Bio signal based: makes controls obsolete, sensing might be possible as well
bio-signal-based most potential, but VR/AR critical niche roles

## Slide 16: Agenda
General Comparison on different Categories
02
Specific example for bio-signal-based
05
Specific examples for VR
03
Specific example for AR
04
What is the best path forward?
06
Why compare?
01

## Slide 17: Best path forward
End goal:
  Bio-signal-based control of robots with human thoughts
Intermediate steps:
  Gradual development of all three technologies
    VR
      Ability to wear headsets for longer
      Training programs
    AR
      Better integration into glasses
    Bio-signal-based
      Higher reliability necessary to be save to use
Notes: VR: better form factor, faster generation of virtual environments
AR:
Bio-signal-based: more consumer-based products to accelerate development
In industry now: heavily depends on application, look at unique functions, then compare
More objective interdisciplinary metric to compare user metrics

## Slide 18
Thank you!

## Slide 19: Literature
Tesla Artificial Intelligence & Autopilot. (2022). Retrieved 7 February 2023, from https://www.tesla.com/AI
Boston Dynamics Spot Product Page. (2022). Retrieved 7 February 2023, from https://www.bostondynamics.com/products/spot
Jang, I., Hu, J., Arvin, F., Carrasco, J., & Lennox, B. (2021). Omnipotent Virtual Giant for Remote Human--Swarm Interaction. 2021 30th IEEE International Conference on Robot & Human Interactive Communication (RO-MAN), 488–494. IEEE.
Lipton, J. I., Fay, A. J., & Rus, D. (2017). Baxter’s homunculus: Virtual reality spaces for teleoperation in manufacturing. IEEE Robotics and Automation Letters, 3(1), 179–186.
Frank, J. A., Moorhead, M., & Kapila, V. (2017). Mobile mixed-reality interfaces that enhance human--robot interaction in shared spaces. Frontiers in Robotics and AI, 4, 20.
DelPreto, J., Salazar-Gomez, A. F., Gil, S., Hasani, R., Guenther, F. H., & Rus, D. (2020). Plug-and-play supervisory control using muscle and brain signals for real-time gesture and error detection. Autonomous Robots, 44(7), 1303–1322.
Dianatfar, M., Latokartano, J., & Lanz, M. (01 2021). Review on existing VR/AR solutions in human–robot collaboration. Procedia CIRP, 97, 407–411. doi:10.1016/j.procir.2020.05.259
Meta Shop. (2022). Retrieved 7 February 2023, from https://www.meta.com/de/en/quest/products/quest-2/
Steam Valve Index Shop. (2022). Retrieved 7 February 2023, from https://store.steampowered.com/valveindex
Apple IPad Shop. (2022). Retrieved 7 February 2023, from https://www.apple.com/shop/buy-ipad/ipad
Samsung Tablet Shop. (2022). Retrieved 7 February 2023, from https://www.samsung.com/us/tablets/galaxy-tab-s8/buy/
Open BCI Shop. (2022). Retrieved 7 February 2023, from https://shop.openbci.com/collections/frontpage
Robertson, A. (2019). Google announces a new $999 Glass augmented reality headset. Retrieved 7 February 2023, from https://www.theverge.com/2019/5/20/18632689/google-glass-enterprise-edition-2-augmented-reality-headset-pricing
Robertson, A. (2017). Oculus Rift and Touch are now $200 cheaper. Retrieved 7 February 2023, from https://www.theverge.com/2017/3/1/14779460/oculus-rift-touch-vr-bundle-price-drop-200
Notes: *Please remove the parenthesis in the final version!!